## Slide 1: IP Dect 130db User Setup Cloud

## Slide 2: Configuration
Base Station
1. Method for Base IP Setting
1) Network mode of the base station is set as DHCP by default.
2) Connect a base station to the POE switch and make it get IP address from a DHCP server.
3) On the handset, press [Menu] button and dial *47* to enter “Base Searching mode”.
4) MAC Address of the base station will be shown with IP address obtained by a DHCP server.
5) Connect the base station Web Admin by accessing the IP. (For example, if the acquired IP is 192.168.125.183)
(http://192.168.125.183)
6) Enter ID(admin) and Password(admin)
7) Make sure all bases and handsets are on the latest firmware

## Slide 3: Configuration Country/Time Settings
On the Base select UK, set the Time Server IP address/URL as you prefer and check DST settings
Save and Reboot

## Slide 4: Configuration
Base IP Setting
Click [Network].
Select DHCP or Static IP.
In case of Static IP, enter network information.(IP, Subnet Mask, Default Gateway, DNS)
Click [Save] to save new configuration.
Reboot the base station.

## Slide 5: Configuration
Reseller Portal
The call server IP address can be found Under Customer Info, Phone Setting Info, SIP Phone Registration IP address

## Slide 6: Configuration
Base Station
Server registration
Click Servers, Add Server
Registrar, Outbound Proxy. Enter the SIP Phone Registration IP Address from Phone Setting Info obtained in the Reseller portal.
NAT Adaption : Select Disable or Enable based on the network environment
Codec Priority : Remove G.722 and adjust the Codec Priority. (G.711A  G.711U)
Click [Save] to save new server information.

## Slide 7: Registration
On Reseller portal
1. Ordering GDC-800H/110dh handset
1) Order request from reseller 800H or 110dh
2) Wait for confirmation from Pragma
3) Order Final Confirm from reseller

## Slide 8: Registration
On Customer Manager portal
Select User, User Setup
Enter User Information
In Device tab select Phone GDC-800H/110dh
Enter Authentication ID to match User ID. Add Password.(Mandatory). MAC Address selection is not required
Important, ensure a secure password is set, include more than 3 types, lower case, upper case, number, symbol
Save.

## Slide 9: Registration
At Base
1. Handset registration
1) Click [Extensions] in menu and [Add extension].

## Slide 10: Registration
At Base
Extension: Enter User ID (Tenant Prefix + Extension Number) defined in Customer Manager portal, User, User Setup, Device
Authentication User Name: Enter (Authentication ID defined in Customer Manager portal)
Enter Authentication Password. (defined in Customer Manager Portal )
Click [Save].
Note. Make sure there are no spaces in these fields, especially when using copy and paste from Customer Manager Portal. Otherwise this can cause registration to fail

## Slide 11: Registration
At Base
Handset registration
In Extensions select extension to register
Click “Register Handset(s).
Base station is waiting for the GDC-800H/110dh handset registration request.

## Slide 12: Registration
At Base and Handset
At Handset
Press [Menu] button.
Select [Connectivity] button.
Select [Register] button.
Enter AC code. (0000)
Click [OK].
Handset displays Name & User ID
Base shows registered

## Slide 13: End Thank you
Go to www.wearepragma.co.uk for more information