## Slide 1: IP Dect 130dB User Setup UCP/eMG80

## Slide 2: Configuration Find Base IP address and login
Base Station
Method for Base IP Setting
1) Network mode of the base station is set as DHCP by default. So you need a DHCP server on the network.
2) Connect a base station to the POE switch and make it get IP address from a DHCP server.
3) On the handset, press [Menu] button and dial *47* to enter “Base Searching mode”.
4) MAC Address of the base station will be shown with IP address obtained by a DHCP server.
5) Connect the base station Web Admin by accessing the IP. (For example, if the acquired IP is 192.168.4.121)
(http://192.168.4.121)
6) Enter ID(admin) and Password(admin).

## Slide 3: Configuration Country/Time Settings
On the Base select UK, set the Time Server IP address/URL as you prefer and check DST settings
Save and reboot

## Slide 4: Configuration
Base IP Setting
Click [Network].
Select DHCP or Static IP.
In case of Static IP, enter network information.(IP, Subnet Mask, Default Gateway, DNS)
Click [Save] to save new configuration.
Reboot the base station.

## Slide 5: Configuration Add Call Server
Call Server registration
Click [Servers] and enter the UCP IP Address in Registrar
NAT Adaption : Select Disable or Enable based on the network environment
Remove G722 codec if not used, note G722 requires double the channels. Codec Priority : Adjust the Codec Priority. (G.711A  G.711U)
Click [Save] to save new server information.

## Slide 6: Registration
UCP / eMG80
On UCP/eMG80 PGM443 add the ID (that would be the extension number) ,the password and the desired number (also extension number and available in PGM105)

## Slide 7: Configuration Handset Registration
At Base
1. Handset registration
1) Click [Extensions] in menu and [Add extension].

## Slide 8: Configuration Handset Registration
At Base
Enter Extension number. (same as in PGM443)
Enter Authentication User Name. (same as in PGM443)
Enter Authentication Password. (same as in PGM443)
Click [Save].

## Slide 9: Configuration Handset Registration
At Base
1. Handset registration
Check the desired handset and Click “Register Handset(s).
State changes to enabled and the base is waiting for the handset request

## Slide 10: Configuration Handset Registration
At Handset
Press [Menu] button.
Select [Connectivity] button.
Select [Register] button.
Enter AC code. (0000)
Click [OK].
Phones says registering
Front screen displays the extension number
On 130dB confirm extension registration as shown
At Base

## Slide 11: Configuration Repeater Registration
From repeaters web select “Add Repeater.

## Slide 12: Configuration Repeater Registration
Select DECT sync mode. Manually: User controlled by manually assign “Repeater RPN” and “DECT sync source RPN” Local Automatical: Repeater controlled by auto detects best base signal and auto assign RPN
Then tick check box and select Register Repeater

## Slide 13: Configuration Repeater Registration
Repeater LED will change from flashing green to solid green and the repeater will show as present in the State column

## Slide 14: End